## Slide 1
Work-let Name: Vector implementation of 3D convolution on CV32E40P core by OpenHW
Worklet Details
Worklet ID: 24CT010CITB
College Name: Cambridge Institute of Technology
  Successful implementation of vector 3D convolution on CV32E40P core.
  Verification of Results through simulation and testing.
Next Steps
Further optimization
Integration with OpenHW
KPIs achieved till now
Succesfull implementation of 3D convolution.
Verification and testing using Pulp simulator.
Key Achievements/ Outcome till now
Challenges or issues faced during the implementation
i.e Debugging
Any Challenges/ Issues faced
Date: 21-04-2025

## Slide 2
Work-let Name: Vector implementation of 3D convolution on CV32E40P core by OpenHW
Worklet Details
Worklet ID: 24CT010CITB
College Name: Cambridge institute of Technology
Any Anticipated Break (Due to exams etc)
Lab internal scheduled on 24/04/25
Internal scheduled on 23/05/25 to 26/05/25
Resource Requirement Identified with Status
Access to GCC toolchain for RISC-V and system libraries
Power profiling tools (if hardware is used)
Kernel sliding data is self-collected
No dataset used; self-implemented kernel validated with synthetic 3D inputs
Data Collection Information
Github Repository Link and PRISM Portal Registration Status
Samsung prism registration is done waiting for approval
Github link waiting for access
Date: 21-04-2025

## Slide 3
Work-let Name: Vector implementation of 3D convolution on CV32E40P core by OpenHW
Worklet Details
Worklet ID: 24CT010CITB
College Name: Cambridge institute of Technology
Date: 21-04-2025

## Slide 4
Work-let Name: Vector implementation of 3D convolution on CV32E40P core by OpenHW
Worklet Details
Worklet ID: 24CT010CITB
College Name: Cambridge institute of Technology
Date: 21-04-2025
BLOCK DIAGRAM

## Slide 5
Work-let Name: Vector implementation of 3D convolution on CV32E40P core by OpenHW
Worklet Details
Worklet ID: 24CT010CITB
College Name: Cambridge institute of Technology
Date: 21-04-2025
FORMULA :
The 3D convolution of an input volume I with a kernel K can be defined
Where:
I is the input volume (3D)
K is the 3D kernel/filter
Dk​, Hk​, and Wk​ are the Depth, height, and width of the kernel
O(x,y,z) is the Output value at position (x,y,z)

## Slide 6
Work-let Name: Vector implementation of 3D convolution on CV32E40P core by OpenHW
Worklet Details
Worklet ID: 24CT010CITB
College Name: Cambridge institute of Technology
Date: 21-04-2025
STEPS:
1. Apply Padding:
Extend the input tensor by adding zeros along the edges according to the padding values
2. Compute Output size:

## Slide 7
Work-let Name: Vector implementation of 3D convolution on CV32E40P core by OpenHW
Worklet Details
Worklet ID: 24CT010CITB
College Name: Cambridge institute of Technology
Date: 21-04-2025
3D Convolution Algorithm:
Input tensor of size (D_in, H_in, W_in)
Kernel of size (D_k, H_k, W_k)
Stride = (s_d, s_h, s_w)
Padding = (p_d, p_h, p_w)

## Slide 8
Work-let Name: Vector implementation of 3D convolution on CV32E40P core by OpenHW
Worklet Details
Worklet ID: 24CT010CITB
College Name: Cambridge institute of Technology
Date: 19-04-2025
Kernel Sliding Method:

## Slide 9
Work-let Name: Vector implementation of 3D convolution on CV32E40P core by OpenHW
Worklet Details
Worklet ID: 24CT010CITB
College Name: Cambridge institute of Technology
Date: 19-04-2025
Program:
#include <stdio.h>
#include<printf.h>
#define IN_SIZE 5#define KERNEL_SIZE 3
#define OUT_SIZE (IN_SIZE - KERNEL_SIZE + 1)
int main()
{
int input[IN_SIZE][IN_SIZE][IN_SIZE] = {
{
{1, 2, 3, 4, 5},
{6, 7, 8, 9, 10},
{11, 12, 13, 14, 15},
{16, 17, 18, 19, 20},
{21, 22, 23, 24, 25}
},
{
{2, 3, 4, 5, 6},
{7, 8, 9, 10, 11},
{12, 13, 14, 15, 16},
{17, 18, 19, 20, 21},
{22, 23, 24, 25, 26}
},
{
{3, 4, 5, 6, 7},
{8, 9, 10, 11, 12},
{13, 14, 15, 16, 17},
{18, 19, 20, 21, 22},
{23, 24, 25, 26, 27} },
{19, 20, 21, 22, 23},
{24, 25, 26, 27, 28} },
,{
{5, 6, 7, 8, 9},
{10, 11, 12, 13, 14},
{15, 16, 17, 18, 19},
{20, 21, 22, 23, 24},
{25, 26, 27, 28, 29} } };
int kernel[KERNEL_SIZE][KERNEL_SIZE][KERNEL_SIZE] = {
{
{1, 0, -1}, {1, 0, -1}, {1, 0, -1}
},
{
{0, 1, 0},
{0, 1, 0},
0, 1, 0} },

## Slide 10
Work-let Name: Vector implementation of 3D convolution on CV32E40P core by OpenHW
Worklet Details
Worklet ID: 24CT010CITB
College Name: Cambridge institute of Technology
Date: 19-04-2025
Program:
{
{-1, 0, 1},
{-1, 0, 1},
{-1, 0, 1}
} };
int output[OUT_SIZE][OUT_SIZE][OUT_SIZE] = {0}; // 3D Convolution
for (int d = 0; d < OUT_SIZE; d++) {
for (int h = 0; h < OUT_SIZE; h++) {
for (int w = 0; w < OUT_SIZE; w++) {
int sum = 0;
for (int kd = 0; kd < KERNEL_SIZE; kd++) {
for (int kh = 0; kh < KERNEL_SIZE; kh++) {
for (int kw = 0; kw < KERNEL_SIZE; kw++) {
sum += input[d + kd][h + kh][w + kw] * kernel[kd][kh][kw];
}
}
}
output[d][h][w] = sum;
} } }
printf("Output Volume (3x3x3):\n");
for (int d = 0; d < OUT_SIZE; d++) {
printf("Depth %d:\n", d);
for (int h = 0; h < OUT_SIZE; h++) {
for (int w = 0; w < OUT_SIZE; w++) {
printf("%4d ", output[d][h][w]);
}
printf("\n"); }
printf("\n"); }
return 0;
}

## Slide 11
Work-let Name: Vector implementation of 3D convolution on CV32E40P core by OpenHW
Worklet Details
Worklet ID: 24CT010CITB
College Name: Cambridge institute of Technology
Date: 19-04-2025
Output:

## Slide 12
Work-let Name: Vector implementation of 3D convolution on CV32E40P core by OpenHW
Worklet Details
Worklet ID: 24CT010CITB
College Name: Cambridge institute of Technology
Date: 19-04-2025
Output:
Executed cycles | Wall clock time | Simulation speed | frequency
24760 | 12.5 s | 1980.8 | 1.9808 kHz

## Slide 13
Work-let Name: Vector implementation of 3D convolution on CV32E40P core by OpenHW
Worklet Details
Worklet ID: 24CT010CITB
College Name: Cambridge institute of Technology
  Status and future plan : 3D convolution algorithm was analysed mathematically and tested the program.
  Students have learnt the PULP tool for RISC V.
  Latest Literature Review: NA
Professor Comments (To be filled in and presented by professor (Either)
Date: 19-04-2025
  Google collab(GITHUB)
COMPUTATION RESOURCE Details:
[Google Collab/ Kaggle / GPU from College lab with compute hours etc]